Get started with Wappsto:bit!

For those who already know and have used micro: bit

What is Wappsto: bit?

Wappsto: bit is an accessory for micro:bit, which connects it with the internet platform Wappsto.com, where you, among other things, can view and control projects from.

Purpose:

We will set up the Wappsto:bit, and get to know it a bit, through a few beginner projects.

Required equipment:

Computer with internet connection
Smartphone (recommended, but not required)
Wappsto: bit with power supply

Micro:bit with USB cable

# Task 1: Setup

Purpose:

To be able to use Wappsto: bit, we must first have it set up and connected it to the internet. Fortunately, it's easy.

Tutorial:

- Go to the website: bit.wappsto.com on the computer.

- Tap Setup at the top of the page

- Follow the wizard to the end.

  - If you run into a problem, try going back a few steps in the wizard and try again.

- When the Wappsto: bit lights up green (is online) and can be seen as online on the Wappsto APP or website, it is ready for use. move on to the next task.

# Task 2: Temp: bit

Purpose: 
We will learn to use the Input blocks from the micro:bit's sensors.

That's why we are building a temperature gauge that is connected directly to the internet!

Instructions:

- Jump to bit.wappsto.com and find the beginner project Temp:bit

- Follow the guide to set up the project, in the first block of MakeCode, also write your group number.

- Select 3 locations that you want to research the temperature at, and note where, and the expected temperature, and why that temperature is expected.

| Location |  |  |  |
| --- | --- | --- | --- |
| Temperature (expected) |  |  |  |
| Why? |  |  |  |

- Plug the Wappsto:bit onto a powerbank and take a smartphone on a research trip!

- Measure the temperature for 3 minutes, at each location, use the smartphone to see that the temperature is updated continuously online.

- Return to the classroom and find the dashboard on the wappsto.

- Examine the measurements, what has actually been measured, and if it is different from what is expected, why? Notes below:

| Location |  |  |  |
| --- | --- | --- | --- |
| Temperature (measured) |  |  |  |
| Difference from expectation? |  |  |  |

- Where was the coldest and warmest, and why? Notes below:

- Try to explain the code, what does each part do? Notes next to each item:

# Task 3: Hello World: bit

Purpose: 
We will try to use Wappsto: bits 2-way communication. That's why we’ll make a display that shows messages that we send from the Internet!

Tutorial:

- Jump to bit.wappsto.com and find the beginning of the project Hello World: bit

- Follow the instructions to set up the project,

- Try to write 1 words and notes including what happened:

- Try to write 1 sentence and notes including what happened:

- Try to explain the code, what does each part do? Notes next to each item:

- What is a String Value? (A guess is okay!)

# Exercise 4: Quickly finished?

Take a look at the project catalog at bit.wappsto.com and try out other cool projects!