Learn about Air Quality with Wappsto: bit

What is Wappsto: bit?

Wappsto:bit is an accessory for micro:bit, which connects it with the internet platform Wappsto.com, where you, among other things, can view and control your device from.

Purpose:
Learn about and experiment with self-collected Air Quality data, in particular Co2 level. To show the current Air Quality level in the classroom using the box's LED. Collect historical data directly to the cloud, where data can be easily visualized and analyzed

Necessary equipment:

Computer with internet connection
Smartphone (recommended, but not necessary)
Wappsto: bit with power supply

Micro: bit with USB cable and computer

SCD-30 Co2 Sensor

Programmable LED light

Prepare scissors and tape (electrician tape / insulation tape gives best results).

# Preparation - Build the box and set up Wappsto:bit

Instructions:

Build the box:

- Unpack Wappsto:bit Air Quality kit out and use scissors to cut out the marked holes.

- Tape LED light and Co2 Sensor onto the box as instructed

Setup Wappsto: bit

- Go to the website: bit.wappsto.com on the computer.

- Tap Setup at the top of the page

- Follow the wizard to the end.

  - If you run into a problem, try going back a few steps in the wizard and try again.

- When the Wappsto: bit lights up green (is online) and can be seen as online on the Wappsto APP or website, it is ready for use.

# Experiment # 1 - Baseline

Introduction:

In experiment # 1, we will establish a baseline for the classroom's indoor climate. We do this by letting Wappsto:bit measure for a week, without doing anything else, and then examining the measurements.

Instructions:

- Jump to bit.wappsto.com and find the expert project “Indoor climate kit!” and follow the instructions, when choosing between 3 different programs, select “Sample every 5 minutes WITHOUT LED light”.

- Have Wappsto: bit Indoor climate box lit in the classroom, and otherwise do as you are used to for 1 week.

- After 1 week, log in to Wappsto again and look at data from the last week on the dashboard.

- Have a loose talk in class about what CO2 level, humidity and temperature are and do.

  - What is co2? How much CO2 is there normally and what does an elevated level mean for our body?

  - What do we really know about humidity?

  - What is a cold and hot indoor temperature? What is nice and what is not nice?

- Analyze and discuss trends

  - When is CO2 level at its highest?

  - When is Co2 lowest? And when does it fall the fastest?

  - Is there suddenly a lot of elevated humidity outside of school hours? Then there is probably someone who washes the floor :-)

  - Can you see a connection between the humidity and the weather?

# Experiment # 2 - LED light and window opening

Introduction:

In experiment # 2, we will turn on the LED lights in the Wappsto:bit box, while measuring. The 3 LED lights on the front will change color and show if the air quality becomes poor, so we can open a window.

Instructions:

- Jump to bit.wappsto.com and find the expert project “Indoor climate kit!” and follow the instructions when choosing between 3 different programs, select “Sample every 5 minutes WITH LED light”.

- Have Wappsto: bit indoor climate box lit in the classroom for a week, but use the LED lights for e.g. to open windows when the co2 level is too high. Appoint a daily dux who is responsible for opening windows.

- Examine data, discuss and analyze trends after a week

  - What are the primary differences from Experiment # 1?

  - Has it helped on air quality?

# Experiment # 3 - How fast is the CO2 level rising?

Introduction:

In experiment # 3 we will see how 1 or more people affect the Co2 level and whether it matters or not how active they are.

Instructions:

- Jump to bit.wappsto.com and find the expert project “Indoor climate kit!” and follow the instructions when choosing between 3 different programs, select “Sample every ½ minute WITH LED light and On / Off function*”.

- Find a smaller room, broom closet or bathroom and place the Wappsto: bit indoor climate meter in it.

- Experiment with how fast you can get CO2 levels to rise, try the following and air out between the experiments:

  - 1 student who does nothing

  - 1 student who makes jumping jacks

  - Several students who do nothing (experiments several times, with 1 extra student per experiment) .

  - More students making jumping jacks

- Analyze and discuss

  - Is there a big difference between doing nothing or making jumping jacks?

  - Does the number of students in the room matter the most, or do you make jumping jacks?

# Experiment # 4 - Co2 from the cars on the school road

Introduction:

In experiment # 4, we will investigate whether rush hour on the school road can be seen from the CO2 level.

Instructions:

- Jump to bit.wappsto.com and find the expert project “Indoor climate kit!” and follow the instructions when choosing between 3 different programs, select “Sample every 5 minutes WITHOUT LED light”.

- Attach the Wappsto: bit to an external battery / power bank so that it can be used outside. Then it should be put outside, close to the school road, where it does not blow away, get wet, or stolen. It can e.g. be placed outside a window on the 1st floor where it does not fall down from.

- Let the Wappsto: bit measure for 1 day or longer, perhaps until it runs out of battery.

- Then discuss and analyze trends

  - Can you see an increased CO2 level in the morning and in the afternoon when there is the most traffic?

  - If you can see an increased CO2 level, how much does it increase then? And how long does it take from the highest until it is at a normal level again?